California State Polytechnic University, Pomona

Aerospace Engineering Department

ARO 309 – Astronautics and Spacecraft Design

Quiz – 01 SOLUTION

- (20 points; 2 points per sub-questions) An Earth orbiter has a periapsis radius of 7,000 km and an apoapsis radius of 15,000 km. Use (Earth = GMEarth = 398,600 km3/s2. Find:

  - eccentricity,

  - semi-major axis,

  - angular momentum,

  - energy of the orbit,

  - apoapsis velocity,

  - periapsis velocity,

  - orbit period,

  - flight path angle when ( = 30 deg,

  - radius when ( = 30 deg,

  - velocity (speed, v) when ( = 30 deg,

- (5 points) How long does it take for a spacecraft in the orbit above to travel from periapsis (( = 0 deg) to ( = 30 deg (therefore Δ(=30 deg). Hint: Use Kepler’s Equaiton for elliptical orbits.