California State Polytechnic University, Pomona

Aerospace Engineering Department

ARO 309 – Astronautics and Spacecraft Design

Homework – 01

Due Wednesday 1/22

- Integrate the following state around the Earth ((Earth = 398,600 km3/s2) for 24 hours (86400 sec). Use the Matlab file provided (see below) or write your own integrator.

X0 = [ 8000  0  6000  0  5  5 ]

(units are in km for position and km/s for velocity)

- Plot the trajectory [If using Matlab: use “plot3” command. Remember type ‘axis equal’ after plotting]. Turn in the printing of the trajectory.

- The equations are suppose to be for a ‘2-body’ orbit where the solution are conics.

  - Why aren’t the solutions purely conics in the plot?

  - What can you do in Matlab to make it look more conic?

- What happens when you change the initial state below? [Just a short description describing what you see plotted.]

X0 = [ 8000  0  6000  0  6  5 ]

X0 = [ 8000  0  6000  0  7  5 ]

X0 = [ 8000  0  6000  0  6.4  0 ]

- What happens when you change the gravitational constant (() of the planet? What happens to your plot in (part 1) when ( is change to:

  - 42,828 km3/s2 (Mars GM)

  - 2 x Earth GM

NOTE: the Matlab files are placed on http://www.trylam.com/2014w_aro309/ and the files are called: twobodyRUN.m and twobodyEOM.m.  The main executable is “twobodyRUN.m”. After opening Matlab just type “twobodyRUN” on the command line.