California State Polytechnic University, Pomona

Aerospace Engineering Department

ARO 309 – Astronautics and Spacecraft Design

Homework – 02

Due Monday 1/27

- From HW#1 Part 1 Find

  - Angular momentum vector, h

  - Angular momentum magnitude, h

  - Specific energy,

  - Eccentricity vector, e

  - Eccentricity (magnitude), e

  - Initial True Anomaly,

  - Radial Velocity,

  - Normal Component Velocity,

  - Flight path angle,

  - Semi-major axis, a

  - Orbit period, T

  - Periapsis and Apoapsis range,

  - Periapsis and Apoapsis speed,

- From HW#1 Part 1

  - Find position and velocity vectors (r and v) for a change in true anomaly of 20 degrees ().

  - Find the angular momentum (h) and specific energy () for the new r and v. from 2.a.

  - How does 2.b. compare to the values from 1.b and 1.c ?