California State Polytechnic University, Pomona

Aerospace Engineering Department

ARO 309 – Astronautics and Spacecraft Design

Homework – 03

Due Monday 1/29

- From HW#1a the initial state is given as y0 = [ 8000 km, 0 km, 6000 km, 0 km/s, 5 km/s, 5 km/s ] for an orbit around the Earth.

  - Using a 2nd order Runge-Kutta algorithm (below), compute the state after a single time step of h = 120 sec later. See "week02" lecture notes for example.

  - How does his compare to HW#1a for a total integration time of 120 seconds?

2. 	Problem 3.11 from Curtis (2nd Edition: Section 3.4)

3.	Problem 3.19 from Curtis (2nd Edition: Section 3.7)