California State Polytechnic University, Pomona

Aerospace Engineering Department

ARO 309 – Astronautics and Spacecraft Design

Homework – 04

Due Monday 2/10

- [2 points] Problem 4.1 Part b (Curtis: Section 4.3)

- [10 points] Problem 4.4 (Curtis: Section 4.4)

[Note: these are not the classical orbital elements they are looking for, so find h instead of a]

- [20 points] Assuming your spacecraft is in orbit around the Earth and has the following orbital elements at time t0:

  - Calculate the geocentric equatorial position and velocity at time t0 for the above orbital elements above.

  - The orbit advances 1 minute (so delta-t = 60 sec).  Compute the mean motion, the Mean anomaly, the Eccentric anomaly, and the true anomaly after the detla-t (so after 60 seconds).

  - Calculate the position and velocity after the 60 seconds in the perifocal coordinates.

  - Compute the new assuming the affect of J2.  So   and .

  - Now compute the transformation matrix to transfer from the perifocal coordinate system to the geocentric equatorial frame with the updated  from above.

  - What is the new position and velocity vector after the 60 seconds?

  - What is the new set of orbital elements after the 60 seconds?